## Slide 1: Topic 03 – Boolean Logic and Logic Design
Week2: Fall 2016

## Slide 2: Agenda
In this topic, we will build the motivation and background for DIGITAL Logic. Specifically, we will discuss
  Digital versus Analog
  Decimal, Binary, Hexadecimal Notations
  Logic Gates and simple examples of combinational logic designs built with these gates
  Boolean Algebra and Operations
Much of the content for this discussion is taken from our reference text written by Professor Vahid Chapters 1 and 2
  Digital Design, 2nd Ed, by Frank Vahid, Wiley publication, 2010

## Slide 3: What Does “Digital” Mean?
Analog signal
  Infinite (continuous) possible values
    Ex: voltage on a wire created by microphone
value
time
value
time
analog
signal
3
4
2
1
2
digital
signal
Digital signal
  Finite (discrete) possible values
    Ex: button pressed on a keypad
0
1
2
3
4
Possible values:
1.00, 1.01, 2.0000009,
... infinite possibilities
Possible values:
0, 1, 2, 3, or 4.
That’s it.

## Slide 4: Digital Signals with Only Two Values: Binary
Binary digital signal -- only two possible values
  Typically represented as 0 and 1
  One binary digit is a bit
  Binary is popular because
    Transistors, basic digital electric components, operate using two voltages VDD and GROUND
    Storing/transmitting one of two values is easier than three or more
value
time
1
0

## Slide 5: Example of Digitization Benefit
Analog signal (e.g., audio) may lose quality
  Voltage levels not saved/copied/transmitted perfectly
time
Volts
0
1
2
3
original signal
lengthy transmission
(e.g, cell phone)
time
0
1
2
3
received signal
How fix -- higher, lower, ?
lengthy transmission
(e.g, cell phone)
01
10
11
10
11
same
time
01
10
11
10
11
Volts
digitized signal
time
0
1
a2d
Volts
0
1
2
3
d2a
Let bit encoding be:
1 V: “01”
2 V: “10”
3 V: “11”
time
Can fix -- easily distinguish 0s and 1s, restore
0
1
Digitized signal not
perfect re-creation,
but higher sampling
rate and more bits per
encoding brings closer.
a
Digitized version enables near-perfect save/cpy/trn.
  “Sample” voltage at particular rate, save sample using bit encoding
  Voltage levels still not kept perfectly
  But we can distinguish 0s from 1s

## Slide 6: How Do We Encode Data as Binary for Our Digital System?
Some inputs inherently binary
  Button: not pressed (0), pressed (1)
Some inputs inherently digital
  Just need encoding in binary
  e.g., multi-button input: encode red=001, blue=010, ...
Some inputs analog
  Need analog-to-digital conversion
  As done in earlier slide -- sample and encode with bits
0
button
1
g
r
een
black
blue
r
ed
0
0
0
r
ed
0
1
0
g
r
een
black
blue
1
0
0
g
r
een
black
blue
r
ed
temperature
sensor
air
0
0
1
1
0
0
0
0
33 degrees
a
sensors and
other inputs
Digital System
actuators and
other outputs
A2D
D2A
analog
phenomena
electric
signal
digital
data
digital
data
electric
signal
digital
data
digital
data

## Slide 7: How to Encode Numbers: Binary
Each position represents a quantity; symbol in position means how many of that quantity
  Base ten (decimal)
    Ten symbols: 0, 1, 2, ..., 8, and 9
    More than 9 -- next position
      So each position power of 10
    Nothing special about base 10 -- used because we have 10 fingers
  Base two (binary)
    Two symbols: 0 and 1
    Each position power of 2
2
4
2
3
2
2
1
0
1
2
1
2
0
10
4
10
3
10
2
5
2
3
10
1
10
0
Q: How much?
+
=
4
1
5
+
=

## Slide 8: Converting from Decimal to Binary: Subtraction Method (Easy for Humans)
Goal
  Get the binary weights to add up to the decimal quantity
    Work from left to right
Desired decimal number: 12
1
2
4
8
16
32
1
=32
too much
1
2
4
8
16
32
0
=16
too much
1
a
1
2
4
8
16
32
0
=8
ok, keep going
0
1
1
2
4
8
16
32
0
=8+4=12
DONE
0
1
1
1
2
4
8
16
32
0
answer
0
1
1
0
0
1
2
4
8
16
32

## Slide 9: Converting from Decimal to Binary: Subtraction Method (Easy for Humans)
Subtraction method
  Go from LEFT to RIGHT
  Subtract a selected binary weight from the (remaining) quantity
    Then, we have a new remaining quantity, and we start again (from the present binary position)
    Stop when remaining quantity is 0
Remaining quantity: 12
1
2
4
8
16
32
1
32 is
too much
1
2
4
8
16
32
0
16 is
too much
1
1
2
4
8
16
32
0
12 – 8 = 4
0
1
1
2
4
8
16
32
0
4-4=0
DONE
0
1
1
1
2
4
8
16
32
0
answer
0
1
1
0
0
1
2
4
8
16
32

## Slide 10: Converting from Decimal to Binary
1.
P
ut 1 in highest pla
c
e
P
la
c
e 32
t
oo bi
g
, but 16
w
o
r
k
s
.
2. Upd
a
t
e decimal number
D
ecimal not
z
e
r
o
,
r
etu
r
n
t
o
S
t
ep 1
1.
P
ut 1 in highest pla
c
e
N
e
x
t pla
c
e is 8,
t
oo big (8>7)
4
w
o
r
ks (4<7)
2. Upd
a
t
e decimal number
D
ecimal number not
z
e
r
o
,
r
etu
r
n
t
o
S
t
ep 1
1.
P
ut 1 in highest pla
c
e
N
e
x
t pla
c
e is 2,
w
o
r
ks (2<3)
2. Upd
a
t
e decimal number
D
ecimal not
z
e
r
o
,
r
etu
r
n
t
o
S
t
ep 1
1.
P
ut 1 in highest pla
c
e
N
e
x
t pla
c
e is 1,
w
o
r
ks (1=1)
2. Upd
a
t
e decimal number
D
ecimal number is
z
e
r
o
, done
D
ecimal
Bina
r
y
(cu
r
r
e
n
t
v
alue
is 16)
23
1
16
–16
7
–4
3
0
1
0
8
0
4
0
2
(cu
r
r
e
n
t
v
alue
is 20)
16
1
0
1
0
8
1
4
0
2
–2
1
–1
0
(cu
r
r
e
n
t
v
alue
is 22)
16
1
0
1
0
8
1
4
1
2
(cu
r
r
e
n
t
v
alue
is 23)
16
1
1
1
0
8
1
4
1
2
Q: Convert the number “23” from decimal to binary
23
-16
7
A: Remaining quantity
Binary Number
23
32
16
8
4
2
1
0
0
0
0
0
0
32
0
16
1
8
0
4
0
2
0
1
0
7
-4
3
4
-2
1
32
0
16
1
8
0
4
1
2
1
1
0
32
0
16
1
8
0
4
1
2
1
1
1
a
1
-1
0
Done! 23 in decimal is 10111 in binary.
32
0
16
1
8
0
4
1
2
0
1
0
8 is more than 7, can’t use

## Slide 11: Base Sixteen: Another Base Sometimes Used by Digital Designers
Nice because each position represents four base two positions
  Used as compact means to write binary numbers
Known as hexadecimal, or just hex
16
4
16
3
16
2
8
A
F
8
1000
1010
1111
A
F
16
1
16
0
0000
0001
0010
0011
0100
0101
0110
0111
0
1
2
3
4
5
6
7
h
e
x
bina
r
y
1000
1001
1010
1011
1100
1101
1110
1111
8
9
A
B
C
D
E
F
h
e
x
bina
r
y
Q: Write 11110000 in hex
F
0

## Slide 12: Combinational Circuits
Combinational
digital circuit
1
a
b
1
F
0
1
a
b
?
F
0
Let’s learn to design digital circuits
We’ll start with a simple form of circuit:
  Combinational circuit
    A digital circuit whose outputs depend solely on the present combination of the circuit inputs’ values
Digital circuit
Sequential
digital circuit

## Slide 13: Switches
A switch has three parts
  Source input, and output
    Current wants to flow from source input to output
  Control input
    Voltage that controls whether that current can flow
“off”
“on”
output
source
input
output
source
input
control
input
control
input
(
b
)
Transistor: Most elementary Digital Device acts like a binary switch – ON or OFF

## Slide 14: The CMOS Transistor
CMOS transistor
  Basic switch in modern ICs
does not
conduct
0
conducts
1
gate
nMOS
does not
conduct
1
gate
pMOS
conducts
0
Silicon -- not quite a conductor or insulator:
Semiconductor
a

## Slide 15: Boolean Logic Gates Building Blocks for Digital Circuits (Because Switches are Hard to Work With)
“Logic gates” are better digital circuit building blocks than switches (transistors)
  Why?...
Notes: Note the power of abstraction which allows us to simplify the object and only deal with the “WHAT” instead of the “HOW”

## Slide 16: Boolean Algebra and its Relation to Digital Circuits
Need to know Boolean algebra to learn how logic gates work
“Traditional” algebra
  Variable represent real numbers
  Operators operate on variables, return real numbers
Boolean Algebra
  Variables represent 0 or 1 only
  Operators return 0 or 1 only
  0 could also be interpreted as “FALSE” and 1 could also be interpreted as TRUE
  Basic operators
    NOT: NOT a returns the opposite of a (1 if a=0, 0 if a=1)
    AND: a AND b returns 1 only when both a=1 and b=1
    OR: a OR b returns 1 if either (or both) a=1 or b=1
a
0
0
1
1
b
0
1
0
1
AND
0
0
0
1
a
0
0
1
1
b
0
1
0
1
OR
0
1
1
1
a
0
1
NOT
1
0

## Slide 17: Boolean Algebra and its Relation to Digital Circuits
Developed mid-1800’s by George Boole to formalize human thought
  Ex: “I’ll go to lunch if Mary goes OR John goes, AND Sally does not go.”
    Let F represent my going to lunch (1 means I go, 0 I don’t go)
    Likewise, m for Mary going, j for John, and s for Sally
    Then F = (m OR j) AND NOT(s)
a
0
0
1
1
b
0
1
0
1
AND
0
0
0
1
a
0
0
1
1
b
0
1
0
1
OR
0
1
1
1
a
0
1
NOT
1
0

## Slide 18: Evaluating Boolean Equations
Evaluate the Boolean equation F = (a AND b) OR (c AND d) for the given values of variables a, b, c, and d:
  Q1: a=1, b=1, c=1, d=0.
    Answer: F = (1 AND 1) OR (1 AND 0) = 1 OR 0 = 1.
  Q2: a=0, b=1, c=0, d=1.
    Answer: F = (0 AND 1) OR (0 AND 1) = 0 OR 0 = 0.
  Q3: a=1, b=1, c=1, d=1.
    Answer: F = (1 AND 1) OR (1 AND 1) = 1 OR 1 = 1.
a
a
0
0
1
1
b
0
1
0
1
AND
0
0
0
1
a
0
0
1
1
b
0
1
0
1
OR
0
1
1
1
a
0
1
NOT
1
0

## Slide 19: Converting to Boolean Equations
Convert the following English statements to a Boolean equation
  Q1. F is TRUE if a is 1 and b is 1.
    Answer: F = a AND b
  Q2. F is TRUE if either of a or b is 1.
    Answer: F = a OR b
  Q3. F is TRUE if both a and b are not 0.
    Answer: F = a OR b
  Q4. F is true if a is 1 and b is 0.
    Answer: F = a AND NOT(b)
a

## Slide 20: Converting to Boolean Equations
A fire sprinkler system should spray water if high heat is sensed and the system is set to enabled.
  Answer: Let Boolean variable h represent “high heat is sensed,” e represent “enabled,” and F represent “spraying water.”
  Then an equation is: F = h AND e.
A car alarm should sound if the alarm is enabled, and either the car is shaken or the door is opened.
  Answer: Let a represent “alarm is enabled,” s represent “car is shaken,” d represent “door is opened,” and F represent “alarm sounds.”
  Then an equation is: F = a AND (s OR d).
a

## Slide 21: Relating Boolean Algebra to Digital Design
Implement Boolean operators using transistors
  Call those implementations logic gates.
  Let’s us build circuits by doing math -- powerful concept
x
0
0
1
1
y
0
1
0
1
F
0
0
0
1
x
0
0
1
1
y
0
1
0
1
F
0
1
1
1
x
0
1
F
1
0
F
x
x
y
F
OR
N
O
T
F
x
y
AND
0
1
y
x
x
y
F
1
0
F
x
Symbol
Truth table
Transistor
circuit
0
1
x
y
F
y
x

## Slide 22: Logic Gate Timing Diagrams
In reality, logic gates have associated switching delays and therefore Logic Gate Timing Diagrams will show a little time skew of the output to the switching of its inputs
0
1
1
0
time
F
x
1
0
x
y
F
1
1
0
0
time
OR
AND

## Slide 23: Building Circuits Using Gates
Recall Chapter 1 motion-in-dark example
  Turn on lamp (F=1) when motion sensed (a=1) and no light (b=0)
  F = a AND NOT(b)
  Build using logic gates, AND and NOT, as shown
  We just built our first digital circuit!

## Slide 24: Example: Converting a Boolean Equation to a Circuit of Logic Gates
Convert the following equation to logic gates: F = a AND NOT( b OR NOT(c) )
a
F
(
a
)
a
b
c
F
(
b
)

## Slide 25: Example: Seat Belt Warning Light System
Design circuit for warning light
Sensors
  s=1: seat belt fastened
  k=1: key inserted
  p=1: person in seat
Capture Boolean equation
  person in seat, and seat belt not fastened, and key inserted
Convert equation to circuit
w = p AND NOT(s) AND k
k
p
s
w
BeltWarn

## Slide 26: Some Circuit Drawing Conventions

## Slide 27: Boolean Algebra
Start with notation: Writing a AND b, a OR b, and NOT(a) is tedious
  Use symbols: a * b, a + b, and a’ (in fact, a * b can be just ab).
    Original: w = (p AND NOT(s) AND k) OR t
    New: w = ps’k + t
    While symbols come from regular algebra, don’t say “times” or “plus”

## Slide 28: Boolean Algebra – Operator Precedence
Boolean algebra precedence, highest precedence first.
Symbol Name Description
( ) Parentheses Evaluate expressions nested in parentheses first
’ NOT Evaluate from left to right
* AND Evaluate from left to right
+ OR Evaluate from left to right

## Slide 29: Boolean Algebra Operator Precedence
Evaluate the following Boolean equations, assuming a=1, b=1, c=0, d=1
  F = a * b + c
    Answer: * has precedence over +, so we evaluate the equation as F = (1 *1) + 0 = (1) + 0 = 1 + 0 = 1
  F = ab + c.
    Answer: the problem is identical to the previous problem, using the shorthand notation for *
  F = ab’
    Answer: we first evaluate b’ because NOT has precedence over AND, resulting in F = 1 * (1’) = 1 * (0) = 1 * 0 = 0
a

## Slide 30: Boolean Algebra Operator Precendence
Evaluate the following Boolean equations, assuming a=1, b=1, c=0, d=1.
  F = (ac)’
    Answer: we first evaluate what is inside the parentheses, then we NOT the result, yielding (1*0)’ = (0)’ = 0’ = 1
  F = (a + b’) * c + d’
    Answer: Inside left parentheses: (1 + (1’)) = (1 + (0)) = (1 + 0) = 1. Next, * has precedence over +, yielding (1 * 0) + 1’ = (0) + 1’. The NOT has precedence over the OR, giving (0) + (1’) = (0) + (0) = 0 + 0 = 0.
a

## Slide 31: Boolean Algebra Terminology
Example equation: F(a,b,c) = a’bc + abc’ + ab + c
Variable
  Represents a value (0 or 1)
  Three variables: a, b, and c
Literal
  Appearance of a variable, in true or complemented form
  Nine literals: a’, b, c, a, b, c’, a, b, and c
Product term
  Product of literals
  Four product terms: a’bc, abc’, ab, c
Sum-of-products
  Equation written as OR of product terms only
  Above equation is in sum-of-products form. “F = (a+b)c + d” is not.

## Slide 32: Boolean Algebra Properties
Distributive
  a * (b + c) = a * b + a * c
  a + (b * c) = (a + b) * (a + c)
Associative
  (a + b) + c = a + (b + c)
  (a * b) * c = a * (b * c)
Complement
  a + a’ = 1
  a * a’ = 0
Commutative
  a + b = b + a
  a * b = b * a
Null
  1 + a = a + 1 = 1
  0 * a = a * 0 = 0
Identity
  a + a = 0 + a = a + 0 = a
  a * a = 1 * a = a * 1 = a

## Slide 33: Boolean Algebra Properties: Example use
Show abc’ equivalent to c’ba.
  Use commutative property:
    a*b*c’ = a*c’*b = c’*a*b = c’*b*a = c’ba
Show abc + abc’ = ab.
  Use first distributive property
    abc + abc’ = ab(c+c’)
  Complement property
    Replace c+c’ by 1: ab(c+c’) = ab(1)
  Identity property
    ab(1) = ab*1 = ab
Show x + x’z equivalent to x + z
  Second distributive property
    Replace x+x’z by (x+x’)*(x+z)
  Complement property
    Replace (x+x’) by 1
  Identity property
    replace 1*(x+z) by x+z

## Slide 34: Example that Applies Boolean Algebra Properties
Want automatic door opener circuit (e.g., for grocery store)
  Output: f=1 opens door
  Inputs:
    p=1: person detected
    h=1: switch forcing hold open
    c=1: key forcing closed
  Want open door when
    h=1 and c=0, or
    h=0 and p=1 and c=0
  Equation: f = hc’ + h’pc’
f
h
c
p
DoorOpener

## Slide 35: Example that Applies Boolean Algebra Properties
Found inexpensive chip that computes:
    f = c’hp + c’hp’ + c’h’p
  Can we use it?
    Is it the same as f = c’(p+h)?
Use Boolean algebra:
f = c’hp + c’hp’ + c’h’p
f = c’h(p + p’) + c’h’p (by the distributive property)
f = c’h(1) + c’h’p (by the complement property)
f = c’h + c’h’p (by the identity property)
f = hc’ + h’pc’ (by the commutative property)
Same!

## Slide 36: Boolean Algebra: Additional Properties
Null elements
  a + 1 = 1
  a * 0 = 0
Idempotent Law
  a + a = a
  a * a = a
Involution Law
  (a’)’ = a
DeMorgan’s Law
  (a + b)’ = a’b’
  (ab)’ = a’ + b’
  Very useful!
To prove, just evaluate all possibilities
Circuit
a
b
c
S
Behavior
  Three lavatories, each with sensor (a, b, c), equals 1 if door locked
  Light “Available” sign (S) if any lavatory available
Equation and circuit
  S = a’ + b’ + c’
Transform
  (abc)’ = a’+b’+c’ (by DeMorgan’s Law)
  S = (abc)’
New equation and circuit
Circuit
S
a
b
c
Aircraft lavatory sign example

## Slide 37: Representations of Boolean Functions
A function can be represented in different ways
  Above shows seven representations of the same functions F(a,b), using four different methods: English, Equation, Circuit, and Truth Table
a
a
b
F
F
Circuit 1
Circuit 2
English 1: F outputs 1 when a is 0 and b is 0, or when a is 0 and b is 1.
English 2: F outputs 1 when a is 0, regardless of b’s value
a
0
0
1
1
b
0
1
0
1
F
1
1
0
0
T
he function F
Truth table
Equation 2: F(a,b) = a’
Equation 1: F(a,b) = a’b’ + a’b

## Slide 38: Truth Table Representation of Boolean Functions
Define value of F for each possible combination of input values
  2-input function: 4 rows
  3-input function: 8 rows
  4-input function: 16 rows
Q: Use truth table to define function F(a,b,c) that is 1 when abc is 5 or greater in binary
c
0
0
1
1
0
0
1
1
0
0
1
1
0
0
1
1
d
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
a
0
0
0
0
0
0
0
0
1
1
1
1
1
1
1
1
b
0
0
0
0
1
1
1
1
0
0
0
0
1
1
1
1
F
c
0
1
0
1
0
1
0
1
a
0
0
0
0
1
1
1
1
b
0
0
1
1
0
0
1
1
F
a
0
0
1
1
b
0
1
0
1
F
(
a
)
(
b
)
(
c
)
c
0
1
0
1
0
1
0
1
a
0
0
0
0
1
1
1
1
b
0
0
1
1
0
0
1
1
F
0
0
0
0
0
1
1
1
a

## Slide 39: Converting among Representations
a
0
0
1
1
b
0
1
0
1
F
Inputs
Output
a
'
b
'
a
' b
Can convert from any representation to any other
Common conversions
  Equation to circuit (we did this earlier)
  Truth table to equation (which we can convert to circuit)
    Just OR each input term that should output 1
  Equation to truth table
    Evaluate equation for each input combination (row)
    Creating intermediate columns helps
a
0
0
1
1
b
0
1
0
1
F
1
1
0
0
Inputs
Outputs
F = sum of
a’b’
a’b
Term
F = a’b’ + a’b
c
0
1
0
1
0
1
0
1
a
0
0
0
0
1
1
1
1
b
0
0
1
1
0
0
1
1
F
0
0
0
0
0
1
1
1
Q: Convert to equation
a
F = ab’c + abc’ + abc
ab’c
abc’
abc
1
1
0
0
1
0
0
0
0
1
0
0
a
Q: Convert to truth table: F = a’b’ + a’b

## Slide 40: Canonical Form -- Sum of Minterms
Truth tables too big for numerous inputs
Use standard form of equation instead
  Known as canonical form
  Regular algebra: group terms of polynomial by power
    ax2 + bx + c (3x2 + 4x + 2x2 + 3 + 1 --> 5x2 + 4x + 4)
  Boolean algebra: create sum of minterms
    Minterm: product term with every function literal appearing exactly once, in true or complemented form
    Just multiply-out equation until sum of product terms
    Then expand each term until all terms are minterms

## Slide 41: Canonical Form -- Sum of Minterms
Q: Determine if F(a,b)=ab+a’ is same function as F(a,b)=a’b’+a’b+ab, by converting first equation to canonical form (second already in canonical form)
F = ab+a’ (already sum of products)
F = ab + a’(b+b’) (expanding term)
F = ab + a’b + a’b’ (SAME -- same three terms as other equation)

## Slide 42: Multiple-Output Circuits
Many circuits have more than one output
Can give each a separate circuit, or can share gates
Ex: F = ab + c’, G = ab + bc
a
b
c
F
G
(
a
)
a
b
c
F
G
(
b
)
Option 1: Separate circuits
Option 2: Shared gates

## Slide 43: Multiple-Output Example: BCD to 7-Segment Converter
a = w’x’y’z’ + w’x’yz’ + w’x’yz + w’xy’z + w’xyz’ + w’xyz + wx’y’z’ + wx’y’z
b = w’x’y’z’ + w’x’y’z + w’x’yz’ + w’x’yz + w’xy’z’ + w’xyz + wx’y’z’ + wx’y’z
c = ?

## Slide 44: Combinational Logic Design Process
Step
Description
Step 1
Capture the function
Create a truth table or equations, whichever is most natural for the given problem, to describe the desired behavior of the combinational logic.
Step 2
Convert to equations
This step is only necessary if you captured the function using a truth table instead of equations. Create an equation for each output by ORing all the minterms for that output. Simplify the equations if desired.
Step 3
Implement as a gate-based circuit
For each output, create a circuit corresponding to the output’s equation. (Sharing gates among multiple outputs is OK optionally.)

## Slide 45: Example: Three 1s Detector
Problem: Detect three consecutive 1s in 8-bit input: abcdefgh
    00011101  1 10101011  0 11110000  1
  Step 1: Capture the function
    Truth table or equation?
      Truth table too big: 2^8=256 rows
      Equation: create terms for each possible case of three consecutive 1s
    y = abc + bcd + cde + def + efg + fgh
  Step 2: Convert to equation -- already done
  Step 3: Implement as a gate-based circuit
bcd
def
fgh
abc
cde
efg
y
a
b
c
d
e
f
g
h
a

## Slide 46: Example: Number of 1s Count
Problem: Output in binary on two outputs yz the number of 1s on three inputs
    010  01 101  10 000  00
  Step 1: Capture the function
    Truth table or equation?
      Truth table is straightforward
  Step 2: Convert to equation
    y = a’bc + ab’c + abc’ + abc
    z = a’b’c + a’bc’ + ab’c’ + abc
  Step 3: Implement as a gate-based circuit
a
b
c
a
b
c
a
b
c
a
b
c
z
a
b
c
a
b
c
a
b
y

## Slide 47: More Gates
NAND: Opposite of AND (“NOT AND”)
NOR: Opposite of OR (“NOT OR”)
XOR: Exactly 1 input is 1, for 2-input XOR. (For more inputs -- odd number of 1s)
XNOR: Opposite of XOR (“NOT XOR”)
x
0
0
1
1
y
0
1
0
1
F
1
0
0
1
x
0
0
1
1
y
0
1
0
1
F
0
1
1
0
x
0
0
1
1
y
0
1
0
1
F
1
0
0
0
x
0
0
1
1
y
0
1
0
1
F
1
1
1
0
x
y
x
y
F
F
NOR
NAND
XOR
XNOR
1
0
x
y
F
x
y
1
0
x
x
y
y
F
NAND
NOR
NAND same as AND with power & ground switched
  Why? nMOS conducts 0s well, but not 1s (reasons beyond our scope) -- so NAND more efficient
Likewise, NOR same as OR with power/ground switched
AND in CMOS: NAND with NOT
OR in CMOS: NOR with NOT
So NAND/NOR more common

## Slide 48: Completeness of NAND
Any Boolean function can be implemented using just NAND gates. Why?
  Need AND, OR, and NOT
  NOT: 1-input NAND (or 2-input NAND with inputs tied together)
  AND: NAND followed by NOT
  OR: NAND preceded by NOTs
Likewise for NOR
f = (a’b’)’ = a + b (DeMorgan’s Law)

## Slide 49: Number of Possible Boolean Functions
How many possible functions of 2 variables?
  22 rows in truth table, 2 choices for each
  2(22) = 24 = 16 possible functions
N variables
  2N rows
  2(2N) possible functions
a
0
0
1
1
b
0
1
0
1
0 or 1 2 choices
0 or 1 2 choices
0 or 1 2 choices
0 or 1 2 choices
F
24 = 16
possible functions
f0
0
0
0
0
b
0
1
0
1
a
0
0
1
1
f1
0
0
0
1
f2
0
0
1
0
f3
0
0
1
1
f4
0
1
0
0
f5
0
1
0
1
f6
0
1
1
0
f7
0
1
1
1
f8
1
0
0
0
f9
1
0
0
1
f10
1
0
1
0
f11
1
0
1
1
f12
1
1
0
0
f13
1
1
0
1
f14
1
1
1
0
f15
1
1
1
1
0
a AND b
a
b
a XOR b
a OR b
a NOR b
a XNOR b
b’
a’
a NAND b
1
16 possible outcomes of the truth table as shown in 16 columns below

## Slide 50: Decoders
Decoder: Popular combinational logic building block, in addition to logic gates
  Converts input binary number to one high output
2-input decoder: four possible input binary numbers
  So has four outputs, one for each possible input binary number
Internal design
  AND gate for each output to detect input combination
i0
i1
d0
d1
d2
d3
1
1
1
0
0
0
i0
i1
d0
d1
d2
d3
0
0
0
0
0
1
i0
i1
d0
d1
d2
d3
i0
i1
d0
d1
d2
d3
0
0
1
0
1
0
0
1
0
1
0
0
i0
d0
d1
d2
d3
i1
i1’i0’
i1’i0
i1i0’
i1i0

## Slide 51: Decoders
Decoder with enable e
  Outputs all 0 if e=0
  Regular behavior if e=1
n-input decoder: 2n outputs
i0
i1
d0
d1
d2
d3
1
1
1
0
0
0
i0
i1
d0
d1
d2
d3
0
0
0
0
0
1
i0
i1
d0
d1
d2
d3
i0
i1
d0
d1
d2
d3
0
0
1
0
1
0
0
1
0
1
0
0
i0
i1
d0
d1
d2
d3
e
1
1
1
1
0
0
0
e
i0
i1
d0
d1
d2
d3
0
1
1
0
0
0
0

## Slide 52: Decoder Example
New Year’s Eve Countdown Display
  Microprocessor counts from 59 down to 0 in binary on 6-bit input
  Want illuminate one of 60 lights for each binary number
  Use 6x64 decoder
    4 outputs unused
d0
d1
d2
d3
i0
i1
i2
i3
i4
i5
e
6x64
dcd
d58
d59
d60
d61
d62
d63
0
Happy
New Year
1
2
3
58
59
a
0
1
0
0
0
0
0
0
1
0
0
0
1
0
0
0
0
0
0
1
0
0
0
0
0
0
0
0
0
0
1
0
0
0
0
0
Microprocessor

## Slide 53: Multiplexor (MUX)
Mux: Another popular combinational building block
  Routes one of its N data inputs to its one output, based on binary value of select inputs
    4 input mux  needs 2 select inputs to indicate which input to route through
    8 input mux  3 select inputs
    N inputs  log2(N) selects
  Like a railyard switch

## Slide 54: MUX Internal Design
s0
d
i0
i1
2
×
1
i1
i0
s0
1
d
2
×
1
i1
i0
s0
0
d
2
×
1
i1
i0
s0
d
0
i0 (1*i0=i0)
i0
(0+i0=i0)
1
0
2x1 mux
i0
4
×
1
i2
i1
i3
s1
s0
d
s0
d
i0
i1
i2
i3
s1
4x1 mux
0
a

## Slide 55: MUX Example
City mayor can set four switches up or down, representing his/her vote on each of four proposals, numbered 1, 2, 3, 4
City manager can display any such vote on large green/red LED (light) by setting two switches to represent binary 00, 01, 10, or 11
Use 4x1 mux
i0
4x1
i2
i1
i3
s1
s0
d
1
2
3
4
Mayor’s switches
manager's
switches
Green/
Red
LED
on/off
Proposal

## Slide 56: Muxes Commonly Together -- N-bit Mux
Ex: Two 4-bit inputs, A (a3 a2 a1 a0), and B (b3 b2 b1 b0)
  4-bit 2x1 mux (just four 2x1 muxes sharing a select line) can select between A or B
i0
s0
i1
2
×
1
d
i0
s0
i1
2
×
1
d
i0
s0
i1
2
×
1
d
i0
s0
i1
2
×
1
d
a3
b3
I
0
s0
s0
I
1
4-bit
2x1
D
C
A
B
a2
b2
a1
b1
a0
b0
s0
4
C
4
4
4
c3
c2
c1
c0
is short
f
or
Simplifying
notation:

## Slide 57: N-bit Mux Example
Four possible display items
  Temperature (T), Average miles-per-gallon (A), Instantaneous mpg (I), and Miles remaining (M) -- each is 8-bits wide
  Choose which to display using two inputs x and y
  Use 8-bit 4x1 mux

## Slide 58: Summary
Combinational circuits
  Circuit whose outputs are function of present inputs
Switches: Basic components in digital circuits
Boolean logic gates: AND, OR, NOT -- Better building block than switches
Boolean algebra: uses true/false variables/operators

## Slide 59: Summary
Representations of Boolean functions: Can translate among equations, circuits, and truth tables
Combinational design process: Translate from equation (or table) to circuit through well-defined steps
More gates: NAND, NOR, XOR, XNOR also useful
Muxes and decoders: Additional useful combinational building blocks