## Slide 1: Machine Language
Building a Modern Computer From First Principles
www.nand2tetris.org

## Slide 2: Where are we at?
FOCUS
FOCUS

## Slide 3: How do we communicate with a computer
(Hardware) We can describe a computer using underlying physical components
  OR
(Binary) We can also describe a computer by the abstraction that specifies its machine language capabilities in sequences of 1’s and 0’s
OR
(Assembly) We can also raise the abstraction one level higher with specifications in some mnemonic language

## Slide 4: Machine Language versus High Level Programming Language
Machine (and Assembly) Language exposes us to programming to the “Metal” i.e. real hardware
  High Level Language gives us the generalities of capabilities and power of expression

## Slide 5: So to look back and look ahead
Chapters 1..3 exposed us to the low level components that are used to build our computer (logic gates, arithmetic and datapath components, memory, etc.)
Chapter 4 shows us how to program our computer
Chapter 5 will give a preview of computer architecture
Chapter 6 will teach us about how to construct an assembler

## Slide 6: Outline of our discussion
[Machine Language] Discuss the concept of stored program computer and the abstractions of machine language
[Addressing Modes] Discuss ways to address content for performing operations
[Typical Examples] Examples of typical assembly language commands

## Slide 7: Stored program computer

## Slide 8: Stored Program Computer

## Slide 9: View from the Programmer’s Perspective
The Programmer sees
  Memory
  CPU
  Registers
Goal: Manipulate Memory using processor and Set of Registers
View
  Memory: Addresses and Content
  CPU: fixed set of elementary operations
  Registers: Single Word values (quick access)

## Slide 10: Types of Operations on a computer
Arithmetic and Logic Operations
Fetch and Store Values from and to the memory
Move values from and to the registers
Test Boolean conditions
Etc.

## Slide 11: Memory Hierarchy

## Slide 12: Registers

## Slide 13: Machine Language
Three elements
- Instructions
- Sequence (Program Counter)
- Addressing

## Slide 14: Machine Language: Instructions

## Slide 15: Machine Language: sequence via Program Counter

## Slide 16: Machine Language: Addressing

## Slide 17: Compilation
Ways to ease the machine language use
- create mnemonics and then “assemble” to true machine language

## Slide 18: Mnemonics (assembly language)

## Slide 19: Symbols

## Slide 20: addressing

## Slide 21: Addressing

## Slide 22: Addressing Modes (Examples)

## Slide 23: Input/Output

## Slide 24: Flow Control

## Slide 25: Flow Control - Unconditional
loop
loop

## Slide 26: Flow Control – Conditional Jump
Sometimes we need to jump only if certain condition(s) is(are) met
  JGT R1, 0, LABEL //Jump if R1 > 0
  // do something with negative R1
  LABEL:
    // do something with positive R1

## Slide 27: Typical assembly Commands

## Slide 28: Typical Commands – arithmetic & logic
Add R1, R2, R3 (add R2 and R3 and put result in R1)
AND R1, R2, R3 (bitwise AND R2 and R3 and put result in R1)
ADD R1, R2, Mem(x) (Add R2 and contents of Memory location x and put result in R1)

## Slide 29: Typical Commands - Memory Access
Operations
  Load R1, Mem(x): Load Contents of Mem(x) into R1
  Store Mem(x), R2: Store Contents of R2 into location Mem(x)
Addressing
  Direct: Load R1, MEM[67] (Load contents of memory location 67 into R1)
  Immediate: Load R1, 67 (Load immediate constant 67 into R1)
  Indirect: Load R1, MEM[@R2] (Load contents of Memory location pointed to by R2 into R1]

## Slide 30: Typical Commands - branches
Unconditional
Conditional e.g. Jump to certain address if a condition is met

## Slide 31: Typical Machine Language Commands

## Slide 32: Hack Computer: Hardware

## Slide 33: Hack Computer - Software

## Slide 34: Hack Computer - Control

## Slide 35: Hack Computer - Registers

## Slide 36: HACK Computer (preview)

## Slide 37: The Hack Computer

## Slide 38: More on Hack Computer
Two Instructions
  A (Address): Fix the address on which to operate
  C (Compute): Specify and Perform Operation
CPU runs program that are resident in instruction memory (ROM)
Registers and Memory Data are all 16 bits wide
Addresses are 15 bits for both Instruction and Data Memory
  ie. 32K words
Memory is always accessed by referencing the contents of the A register
  For example: D = M[516] -1 would imply setting A to 516 and then doing a read to memory location 516 via A and subtracting 1 from the read content to write the result to A

## Slide 39: A-Instruction

## Slide 40: The A-Instruction

## Slide 41: A-Instruction: Symbolic and Binary Syntax

## Slide 42: A-Instruction Quiz

## Slide 43: The C-Instruction: Symbolic and Binary Syntax
READ THIS IN SLIDESHOW

## Slide 44: C-Instruction in Entirety

## Slide 45: Quiz

## Slide 46: The C-Instruction

## Slide 47: The C-Instruction (JMP)

## Slide 48: The C-Instruction – More Examples
D = A -1
AD = A+1
@19, D=A
AD = A+D
@5034, M=D-1
@171, D=A; @53, M=D
@7, M=M+1, D=M

## Slide 49: The C-instruction (first approximation)
j 3012
sum 4500
q 3812
arr 20561
Symbol table:
(All symbols and values are arbitrary examples)
Exercise: Implement the following tasks using Hack commands:
sum = 0
j = j + 1
q = sum + 12 – j
arr[3] = -1
arr[j] = 0
arr[j] = 17
etc.
dest = x + y
dest = x - y
dest = x
dest = 0
dest = 1
dest = -1
x = {A, D, M}
y = {A, D, M , 1}
dest = {A, D, M, MD, A, AM, AD, AMD, null}

## Slide 50: Hack Program

## Slide 51: Hack Program: Symbolic and Binary

## Slide 52: Summary – Hack Assembly Instructions

## Slide 53: Hack Assembler

## Slide 54: Hack CPU Emulator

## Slide 55: Hack Programming

## Slide 56: Working with Registers and Memory

## Slide 57: Working with Registers and Memory

## Slide 58: Registers - Quiz

## Slide 59: Hack Program Example: Adding Two Numbers

## Slide 60: Terminating a Program Correctly

## Slide 61: Hack: Built-In Symbols

## Slide 62: Hack: Other built-in symbols

## Slide 63
Control (focus on the yellow chips only)
ALU
Mux
D
A/M
a-bit
D register
A register
A
M
RAM
(selected register)
ROM
(selected register)
PC
Instruction
In the Hack architecture:
ROM = instruction memory
Program = sequence of 16-bit numbers, starting at ROM[0]
Current instruction = ROM[PC]
To select instruction n from the ROM, we set A to n, using the instruction @n
address input
address input

## Slide 64: Coding examples (practice)
Exercise: Implement the following tasks using Hack commands:
goto 50
if D==0 goto 112
if D<9 goto 507
if RAM[12] > 0 goto 50
if sum>0 goto END
if x[i]<=0 goto NEXT.
sum 2200
x 4000
i 6151
END 50
NEXT 120
Symbol table:
(All symbols and values in are arbitrary examples)
Hack commands:
A-command: @value // set A to value
C-command: dest = comp ; jump // dest = and ;jump // are optional
Where:
comp = 0 , 1 , -1 , D , A , !D , !A , -D , -A , D+1 , A+1 , D-1, A-1 , D+A , D-A , A-D , D&A , D|A , M , !M , -M ,M+1, M-1 , D+M , D-M , M-D , D&M , D|M
dest = M , D , MD , A , AM , AD , AMD, or null
jump = JGT , JEQ , JGE , JLT , JNE , JLE , JMP, or null
In the command dest = comp; jump, the jump materialzes if (comp jump 0) is true. For example, in D=D+1,JLT, we jump if D+1 < 0.
Hack convention:
True is represented by -1
False is represented by 0

## Slide 65: IF logic – Hack style
if condition {
code block 1}
else {
code block 2}
code block 3
High level:
D  not condition
@IF_TRUE
D;JEQ
code block 2
@END
0;JMP
(IF_TRUE)
code block 1
(END)
code block 3
Hack:
Hack convention:
True is represented by -1
False is represented by 0

## Slide 66: WHILE logic – Hack style
while condition {
code block 1
}
Code block 2
High level:
(LOOP)
D  not condition
@END
D;JEQ
code block 1
@LOOP
0;JMP
(END)
code block 2
Hack:
Hack convention:
True is represented by -1
False is represented by 0

## Slide 67
Side note (focus on the yellow chip parts only)
ALU
Mux
D
A/M
a-bit
D register
A register
A
M
RAM
(selected register)
ROM
(selected register)
PC
Instruction
address input
address input
In the Hack architecture, the A register addresses both the RAM and the ROM, simultaneously. Therefore:
Command pairs like @addr followed by D=M;someJumpDirective make no sense
Best practice: in well-written Hack programs, a C-instruction should contain
  either a reference to M, or
  a jump directive,
but not both.
Notes: 67

## Slide 68: Complete program example
// Adds 1+...+100.
into i = 1;
into sum = 0;
while (i <= 100){
sum += i;
i++;
}
C language code:
// Adds 1+...+100.
@i // i refers to some RAM location
M=1 // i=1
@sum // sum refers to some RAM location
M=0 // sum=0
(LOOP)
@i
D=M // D = i
@100
D=D-A // D = i - 100
@END
D;JGT // If (i-100) > 0 goto END
@i
D=M // D = i
@sum
M=D+M // sum += i
@i
M=M+1 // i++
@LOOP
0;JMP // Got LOOP
(END)
@END
0;JMP // Infinite loop
Hack assembly code:
Hack assembly convention:
Variables: lower-case
Labels: upper-case
Commands: upper-case

## Slide 69: Symbols in Hack assembly programs
Symbols created by Hack programmers and code generators:
Label symbols: Used to label destinations of goto commands. Declared by the pseudo command (XXX). This directive defines the symbol XXX to refer to the instruction memory location holding the next command in the program (within the program, XXX is called “label”)
Variable symbols: Any user-defined symbol xxx appearing in an assembly program that is not defined elsewhere using the (xxx) directive is treated as a variable, and is “automatically” assigned a unique RAM address, starting at RAM address 16
By convention, Hack programmers use lower-case and upper-case letters for variable names and labels, respectively.
Predefined symbols:
I/O pointers: The symbols SCREEN and KBD are “automatically” predefined to refer to RAM addresses 16384 and 24576, respectively (base addresses of the Hack platform’s screen and keyboard memory maps)
Virtual registers: covered in future lectures.
VM control registers: covered in future lectures.
// Typical symbolic
// Hack code, meaning
// not important
@R0
D=M
@INFINITE_LOOP
D;JLE
@counter
M=D
@SCREEN
D=A
@addr
M=D
(LOOP)
@addr
A=M
M=-1
@addr
D=M
@32
D=D+A
@addr
M=D
@counter
MD=M-1
@LOOP
D;JGT
(INFINITE_LOOP)
@INFINITE_LOOP
0;JMP
Q: Who does all the “automatic” assignments of symbols to RAM addresses?
A: The assembler, which is the program that translates symbolic Hack programs into binary Hack program. As part of the translation process, the symbols are resolved to RAM addresses. (more about this in future lectures)
Notes: 69

## Slide 70: Perspective
Hack is a simple machine language
User friendly syntax: D=D+A instead of ADD D,D,A
Hack is a “½-address machine”: any operation that needs to operate on the RAM must be specified using two commands: an A-command to address the RAM, and a subsequent C-command to operate on it
A Macro-language can be easily developed
A Hack assembler is needed and will be discusses and developed later in the course.