## Slide 1: CPU Pipelining
ACKNOWLEDGMENTS
Vladimir Stojanovic and Nicholas Weaver
http://inst.eecs.Berkeley.edu/~cs61c/sp16

## Slide 2: Gotta Do Laundry
Ann, Brian, Cathy, Dave each have one load of clothes to wash, dry, fold, and put away
  Washer takes 30 minutes
  Dryer takes 30 minutes
  “Folder” takes 30 minutes
  “Stasher” takes 30 minutes to put clothes into drawers
A
B
C
D

## Slide 3: Sequential Laundry
Sequential laundry takes 8 hours for 4 loads
T
a
s
k
O
r
d
e
r
B
C
D
A
30
Time
30
30
30
30
30
30
30
30
30
30
30
30
30
30
30
6 PM
7
8
9
10
11
12
1
2 AM

## Slide 4: Pipelined Laundry
Pipelined laundry takes 3.5 hours for 4 loads!
T
a
s
k
O
r
d
e
r
B
C
D
A
12
2 AM
6 PM
7
8
9
10
11
1
Time
30
30
30
30
30
30
30

## Slide 5: Pipelining Lessons (1/2)
Pipelining doesn’t help latency of single task, it helps throughput of entire workload
Multiple tasks operating simultaneously using different resources
Potential speedup = Number pipe stages
Time to “fill” pipeline and time to “drain” it reduces speedup: 2.3x (8/3.5) v. 4x (8/2) in this example
6 PM
7
8
9
Time
B
C
D
A
30
30
30
30
30
30
30
T
a
s
k
O
r
d
e
r

## Slide 6: Pipelining Lessons (2/2)
Suppose new Washer takes 20 minutes, new Stasher takes 20 minutes. How much faster is pipeline?
Pipeline rate limited by slowest pipeline stage
Unbalanced lengths of pipe stages reduces speedup
Dependencies between stages???
6 PM
7
8
9
Time
B
C
D
A
30
30
30
30
30
30
30
T
a
s
k
O
r
d
e
r

## Slide 7: Execution Steps in Typical Processor Datapath
1) FETCH: Instruction Fetch, Increment PC
2) DECODE: Instruction Decode, Read Registers
3) EXECUTE: Mem-ref: Calculate Address Arith-log: Perform Operation
4) Memory: Load: Read Data from Memory Store: Write Data to Memory
5) Writeback: Write Data Back to Register

## Slide 8: Single Cycle Datapath
PC
instruction
memory
+4
registers
ALU
Data
memory
imm
1. Instruction
Fetch
2. Decode/
Register Read
3. Execute
4. Memory
5. Write Back

## Slide 9: Pipeline registers
1. Instruction
Fetch
2. Decode/
Register Read
3. Execute
4. Memory
5. Write Back
Need registers between stages
  To hold information produced in previous cycle
PC
instruction
memory
+4
registers
ALU
Data
memory
imm

## Slide 10: More Detailed Pipeline

## Slide 11: Example: IF for Load, Store, …

## Slide 12: ID for Load, Store, …

## Slide 13: EX for Load

## Slide 14: MEM for Load

## Slide 15: WB for Load – Oops!
Wrong register number!

## Slide 16: Corrected Datapath for Load

## Slide 17: Pipelined Execution Representation
Every instruction must take same number of steps, so some stages will idle
  e.g. MEM stage for any arithmetic instruction
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
Time
Notes: Each instruction has identical latency!

## Slide 18: Graphical Pipeline Diagrams
Use datapath figure below to represent pipeline:
IF
ID
EX
Mem
WB
ALU
I$
Reg
D$
Reg
1. Instruction
Fetch
2. Decode/
Register Read
3. Execute
4. Memory
5. Write
Back
PC
instruction
memory
+4
Register
File
ALU
Data
memory
imm
MUX
Note: I$ is another way of referring to instruction memory, and D$ refers to Data Memory

## Slide 19: Graphical Pipeline Representation
I
n
s
t
r
O
r
d
e
r
Load
Add
Store
Sub
Or
I$
Time (clock cycles)
I$
ALU
Reg
Reg
I$
D$
ALU
ALU
Reg
D$
Reg
I$
D$
Reg
ALU
Reg
Reg
Reg
D$
Reg
D$
ALU
Reg: left half is write, right half is read
Reg
I$

## Slide 20: Pipelining Performance (1/2)
Assume time for stages is
  100ps for register read or write
  200ps for other stages
What is pipelined clock rate?
  Compare pipelined datapath with single-cycle datapath
Instr | Instr fetch | Register read | ALU op | Memory access | Register write | Total time
lw | 200ps | 100 ps | 200ps | 200ps | 100 ps | 800ps
sw | 200ps | 100 ps | 200ps | 200ps |  | 700ps
add (reg) | 200ps | 100 ps | 200ps |  | 100 ps | 600ps
jeq (reg) | 200ps | 100 ps | 200ps |  |  | 500ps

## Slide 21: Pipelining Performance (2/2)
Single-cycle
Tc = 800 ps
f = 1.25GHz
Pipelined
Tc = 200 ps
f = 5GHz
Here using Tc as “time between completion of instructions.”
Notes: Here using Tc as “time between completion of instructions.”

## Slide 22: Single Cycle Performance
Assume time for actions are
  100ps for register read or write; 200ps for other events
Clock period is?
Instr | Instr fetch | Register read | ALU op | Memory access | Register write | Total time
lw | 200ps | 100 ps | 200ps | 200ps | 100 ps | 800ps
sw | 200ps | 100 ps | 200ps | 200ps |  | 700ps
R-format | 200ps | 100 ps | 200ps |  | 100 ps | 600ps
beq | 200ps | 100 ps | 200ps |  |  | 500ps
Clock rate (cycles/second = Hz) = 1/Period (seconds/cycle)
Notes: 1.25 GHz

## Slide 23: Single Cycle Performance
Assume time for actions are
  100ps for register read or write; 200ps for other events
Clock period is?
Instr | Instr fetch | Register read | ALU op | Memory access | Register write | Total time
lw | 200ps | 100 ps | 200ps | 200ps | 100 ps | 800ps
sw | 200ps | 100 ps | 200ps | 200ps |  | 700ps
R-format | 200ps | 100 ps | 200ps |  | 100 ps | 600ps
beq | 200ps | 100 ps | 200ps |  |  | 500ps
What can we do to improve clock rate?
  We can do deeper pipelines and/or break slowest stages
Will this improve performance as well?
  Normally yes, because throughput will improve. But deeper pipelines can incur higher penalty for pipeline flushes for control dependencies
Notes: 1.25 GHz

## Slide 24: Pipelining – Bringing Realism
Register storage overhead between every pipeline stage
Stalls (waiting for data that is not there yet)
Flushes (loaded ‘wrong’ instructions)

## Slide 25: CPU implementation
Execute logic:
Decode
Execute
Fetch logic:
If there should be a jump, set PC to A else set PC to PC+1
Cycle:
Execute
Fetch
Resetting the computer:
Set reset to 1, then set it to 0.
Chip diagram:
Includes most of the CPU’s execution logic
The CPU’s control logic is hinted: each circled “c” represents one or more control bits, taken from the instruction
The “decode” bar does not represent a chip, but rather indicates that the instruction bits are decoded somehow.

## Slide 26: Register Overhead

## Slide 27: Pipeline Overhead
Logic in some stages takes 200ps and in some 100ps. Clk-Q delay is 30ps and setup-time is 20ps. What is the maximum clock frequency at which a pipelined design can operate?
A: 10GHz
B: 5GHz
C: 6.7GHz
D: 4.35GHz
E: 4GHz
Notes: Frequency is 4 GHZ as it is inverse of the cycle time of 250ps

## Slide 28: Practice question
The 5 stages of the processor have the following latencies:
  Fetch Decode Execute Memory Writeback
  a. 300ps 400ps 350ps 550ps 100ps
  b. 200ps 150ps 100ps 190ps 140ps
Assume that when pipelining, each stage costs 20ps extra for the registers between pipeline stages.
CASE1: Non-pipelined processor: what is the cycle time? What is the latency of an instruction? What is the throughput?
Because there is no pipelining, the cycle time must allow an instruction to go through all stages in one cycle. The latency is the same as cycle time since it takes the instruction one cycle to go from the beginning of fetch to the end of write back. The throughput is defined as 1/CT inst/s.
a. CT = 300 + 400 + 350 + 550 + 100 = 1700ps …….Latency = 1700ps……Throughput = 1/1700 inst/ps
b. CT = 200 + 150 + 100 + 190 + 140 = 780ps…….Latency = 780ps…….Throughput = 1/780 inst/ps

## Slide 29: Practice example: Pipelined case
Case2: Pipelining reduces the cycle time to the length of the longest stage plus the register delay. Latency becomes CT*N where N is the number of stages as one instruction will need to go through each of the stages and each stage takes one cycle. The throughput formula remains the same.
a. CT = 550 + 20 = 570 ps
  Latency = 5 * 570 = 2850ps
  Throughput = 1/570 inst/ps
b. CT = 200 + 20 = 220 ps
  Latency = 5 * 220 = 1100ps
  Throughput = 1/220 inst/ps

## Slide 30: Practice question: what if?
If you could split one of the pipeline stages into 2 equal halves, which one would you choose? What is the new cycle time? What is the new latency? What is the new throughput?
Answer: We would want to choose the longest stage to split in half. The new cycle time becomes the originally 2nd longest stage length. Calculate latency and throughput correspondingly, but remember there are now 6 stages instead of 5.
a. CT = 400 + 20 = 420 ps
  Latency = 6 * 420 = 2520 ps
  Throughput = 1/420 inst/ps
b. CT = 190 + 20 = 210 ps
  Latency = 6 * 210 = 1260 ps
  Throughput = 1/210 inst/ps

## Slide 31: Pipelining – Bringing Realism
Register storage overhead between every pipeline stage
Stalls (waiting for data that is not there yet)
Flushes (loaded ‘wrong’ instructions)

## Slide 32: Data dependencies
Look at these 2 HACK instructions
  I1: A = D + M
  I2: AD = M
What data dependencies do you see in the above simple instruction stream?
Hint: I2 is trying to write into a register which was written to by I1.
What other dependencies do you see?

## Slide 33: Data dependencies
Look at these 2 HACK instructions
  A = D + M
  AD = M
In HACK CPU, we simply execute one instruction at a time
But what if HACK was pipelined in 5 stages?
IF
ID
EX
MEM
WB
I1
C1
C3
C2
C4
C5
I2
I1
I2
I1
I2
I1
I2
I1
Problem with this implementation:
I1 updates register A in cycle C5. I2 needs it in cycle C3!!
So I2 should not be allowed to proceed in the pipe
C6
I2

## Slide 34: Data dependencies
Read After Write (RAW)
  Memory or Register is read after being written to by a prior instruction
  Example: I13 is reading the contents of D that were updated by prior instruction I11
Write After Read (WAR)
  Memory or Register is written to after being read by a prior instruction
  Example: I11 updates register D which was read by prior instruction I9
Write After Write (WAW)
  Memory or Register is written to after being written to by a prior instruction
  Example: I7 updates register D which was updated by prior instruction I5

## Slide 35: do dependencies matter?
Dependencies are immaterial in a non-pipelined CPU implementation (e.g HACK Computer) because we are processing only ONE instruction at a time
However, in a pipelined CPU, more than one instruction can be in the pipeline in a given cycle (at most n instructions in a n-stage pipeline)
The correct values must be read at ALL times
The possibility of an incorrect value being read is called a HAZARD
Not ALL DEPENDENCIES constitute a HAZARD

## Slide 36: Discussion: True and False Dependencies
RAW are true dependencies
WAR and WAW are false dependencies i.e. they are dependencies in name only
RAR are not dependencies since the “RAR dependent” instructions could be swapped without impacting program output unlike WAR or WAW where the program output could be different.

## Slide 37: When does a RAW dependency constitute a hazard?
Read After Write (RAW)
  Memory or Register is read after being written to by a prior instruction
RAW HAZARD: Example: I13 is reading the contents of D that were updated by prior instruction I11
  This dependency will be a hazard because I13 is reading register D in C4 even though the new value of D will not become available until C5!!
IF
ID
EX
MEM
WB
I11
Ci
Ci+2
Ci+1
Ci+3
Ci+4
I12
Ci+5
I13
I11
I12
I13
I11
I12
I13
I11
I12
I13
I11
I12
I13
Ci+6

## Slide 38: How do we fix a RAW Hazard?
We use a technique call “STALL” by not advancing the impacted instruction in the pipeline so as to resolve the RAW hazard
I13 reads the correct value of D written by I11
 | IF | ID | EXE | MEM | WB
Ci | I11 |  |  |  | 
Ci+1 | I12 | I11 |  |  | 
Ci+2 | I13 | I12 | I11 |  | 
Ci+3 | I13 | STALL | I12 | I11 | 
Ci+4 | I13 | STALL |  | I12 | I11
Ci+5 |  | I13 |  |  | I12
Ci+6 |  |  | I13 |  | 
Ci+7 |  |  |  | I13 | 

## Slide 39: When does a RAW dependency NOT constitute a hazard?
Read After Write (RAW)
  Memory or Register is read after being written to by a prior instruction
RAW Dependency: Example: I13 is reading the contents of D that were updated by prior instruction I5
  This dependency will NOT be a hazard because I5 completes execution well in advance of I13

## Slide 40: More discussion on dep and haz
Identify dependencies and hazards in the instruction stream executed in a 5-stage pipelined CPU
RAW |  | WAR |  | WAW | 
I0  I5 |  |  |  |  | 
I5 I7 * |  |  |  | I5  I7 | 
I7  I9 * |  |  |  |  | 
I7  I11* |  | I9 I11; I7 I11 |  | I7 –I 11 | 
Note: * implies a HAZARD
Complete the rest of the
table as exercise

## Slide 41: Generic Example - dependencies
IF
ID
EX
MEM
WB
I1: MUL R1, R2, R3
I2: ADD R6, R1, R6
I3: MUL R1, R5, R6
I4: SUB R4, R1, R2
 | RAW | WAR | WAW
I1  I2 | YES | N/A | N/A
I1  I3 | N/A | N/A | YES
I1  I4 | YES | N/A | N/A
I2  I3 | YES | YES | N/A
INSTRUCTION DEST, SRC1, SRC2

## Slide 42: To Summarize: Dependencies and Hazards
A Dependency is property of program alone
A Hazard is a situation when Dependence results in incorrect program execution
  Hazard is a property of program as well as pipeline

## Slide 43: Example
ADD R1, R1, R2
MUL R2, R2, R4
SUB R6, R2, R6
DIV R10, R6, R10
XOR R11, R11,R1
IF | ID | EX | MEM | WB
XOR | DIV | SUB | MUL | ADD
 | XOR | DIV | SUB | MUL
By the time XOR reads R1, ADD has already completed
and is therefore not a hazard to XOR
What if DIV and XOR were swapped?
INSTRUCTION DEST, SRC1, SRC2

## Slide 44: Pipelining – Bringing Realism
Register storage overhead between every pipeline stage
Stalls (waiting for data that is not there yet)
Flushes (loaded ‘wrong’ instructions)

## Slide 45: Example – Conditional Jump
When I9 executes a Jump, I10, I11, and I12 are already in the pipeline!!
  These need to be FLUSHED and I18 needs to be loaded
 | IF | ID | EXE | MEM | WB
Ci | I7 |  |  |  | 
Ci+1 | I8 | I7 |  |  | 
Ci+2 | I9 | I8 | I7 |  | 
Ci+3 | I10 | I9 | I8 | I7 | 
Ci+4 | I11 | I10 | I9 | I8 | I7
Ci+5 | I12 | I11 | I10 | I9 | I8
Ci+6 | I18 |  |  |  | I9
Ci+7 |  | I18 |  |  | 

## Slide 46: Example: unconditional jump
IF | ID | EX | MEM | WB
JMP | ADD R1, R1,R2 | SUB R6, R6, R7 |  | 
XOR R10, R10, R11 | JMP | ADD R1, R1, R2 | SUB R6, R6, R7 | 
MUL R8, R8, R9 | XOR R10, R10, R11 | JMP | ADD R1, R1, R2 | SUB R6, R6, R7
DIV R4, R4, R5 | MUL R8, R8, R9 | XOR R10, R10, R11 | JMP | ADD R1, R1, R2
Once unconditional JMP executes, it causes MUL and XOR to
Be flushed from the pipe. New Instruction DIV is brought into the PIPE

## Slide 47: Pipelining Topics out of Scope for this offering of 312
Instruction Reordering: Role of Compiler in reducing hazards (LINK)
  Restructure program to eliminate RAW hazards
Forwarding (http://www.cs.utexas.edu/users/mckinley/352/lectures/12.pdf Slide 14 and onwards)
  Forward the results (after EXE) to instructions waiting for the data instead of waiting all the way till the instruction retires (2 cycle gain!)
Register Renaming (LINK)
Out of Order execution (LINK)
These topics can be learnt in CSCE-350

## Slide 48: What to expect from the preceding slide set in the Final Exam?
Be able to name the 5 stages in a simple pipeline and match them to descriptions
Be able to calculate latency, throughput, and clock period for hypothetical examples
Be able to draw pipestage execution for given instruction stream
Answer some general True/False statements limited to material presented in this slide set

## Slide 49: What to expect from the preceding slide set in the Final Exam (contd.)?
Be able to name key overheads in pipeline execution
Calculate pipeline frequency with specified overheads
Identify data dependencies between instructions
Draw pipeline execution diagram for an instruction stream with stalls and flushes