## Slide 1: W2– Operating Systems Architectural Interface, Exception Control flow
CSCE 313 Spring 2017
Reading Reference: Textbook Chapter 1, 2

## Slide 2: Content for this week
CSCE-313 Spring 2017
OS roles and its key challenges (Text: Chap. 1)
Control Flow in a modern computer system (Text: Chap. 2)
  Normal flow of commands and data versus anything that happens “out of the ordinary” .. how do we handle that?
Architectural Interface to the OS (Text: Chap. 2)
  features we design in HW to facilitate the OS to meet some key challenges

## Slide 3: Operating System Roles
CSCE-313 Spring 2017
Referee
  Manage sharing of resources, Protection, Isolation
    Resource allocation, isolation, communication
Illusionist
  Provide clean, easy to use abstractions of physical resources
    Infinite memory, dedicated machine
    Masking limitations, virtualization
Glue
  Common services
    Storage, Window system, Networking
    Sharing, Authorization
    Look and feel
Application Programs/Processes
storage
Processor
Memory
user1
user2
user3
user4
return
user1
user2
user3
user4
Packet I/O

## Slide 4: What, then, is an Operating System?
CSCE-313 Spring 2017
The OS controls and coordinates the use of system resources.
Primary goal: Provide a convenient environment for a user to access the available resources (CPU, memory, I/O)
  Provide appropriate abstractions (files, processes, ...)
  “virtual machine”
Secondary goal: Efficient operation of the computer system.
Key facets of Resource Management
  Transforming: Create virtual substitutes that are easier to use.
  Multiplexing: Create the illusion of multiple resources from a single resource
  Scheduling: “Who gets the resource when?”

## Slide 5: What an operating system is not
CSCE-313 Spring 2017
  OS is not a language or a compiler
  OS is not a command interpreter / window system
  OS is not a library of commands
  OS is not a set of utilities

## Slide 6: Key OS Challenges
CSCE-313 Spring 2017
Reliability
  Does the system do what it was designed to do?
Availability
    What portion of the time is the system working?
    Mean Time To Failure (MTTF), Mean Time to Repair

## Slide 7: Key OS Challenges
CSCE-313 Spring 2017
Servicability
  Simplicity and Ease of system repair and maintenance
Security
  An OS needs both a security policy (what is permitted) and an enforcement mechanism (only allow permitted actions)
  Can the system be compromised by an attacker?
  Privacy: Data is accessible only to authorized users

## Slide 8: Key OS Challenges
CSCE-313 Spring 2017
Portability
  For programs:
    Application programming interface (API)
    Abstract machine interface
  For the operating system
    Hardware abstraction layer

## Slide 9: Key OS Challenges
CSCE-313 Spring 2017
Performance
  Latency/response time
    How long does an operation take to complete?
  Throughput
    How many operations can be done per unit of time?
  Overhead
    How much extra work is done by the OS?
  Fairness
    How equal is the performance received by different users?
  Predictability
    How consistent is the performance over time?

## Slide 10: Challenges in Modern OSs
Smart Phones
  Responsiveness, security
Embedded Systems
  Reliable
Web Servers
  Supporting billions of requests/sec efficiently
Virtual Machines
  Low overhead and also proper h/w virtualization
Server Clusters
  Hide the clustering details from application programs
1/23/2017

## Slide 11: Challenges in Tomorrow’s OSs
Existing challenges would be more critical
  OSs controlling future self driving cars, or traffic lights need to be absolutely reliable, secure, and efficient
The future of OSs is intertwined with that of emerging computing hardware
  Giant-scale data centers
  Increasing numbers of processors per computer
  Newer portable devices
  Very large scale storage
1/23/2017

## Slide 12: Content for this week
CSCE-313 Spring 2017
OS roles and its key challenges (Text: Chap. 1)
Control Flow in a modern computer system (Text: Chap. 2)
  Normal flow of commands and data versus anything that happens “out of the ordinary” .. how do we handle that?
Architectural Interface to the OS (Text: Chap. 2)
  features we design in HW to facilitate the OS to meet some key challenges

## Slide 13: Traditional UNIX System Structure
CSCE-313 Spring 2017

## Slide 14: Control Flow
CSCE-313 Spring 2017
<startup>
inst1
inst2
inst3
…
instn
<shutdown>
Computers do only one thing
  From startup to shutdown, a CPU simply reads and executes (interprets) a sequence of instructions, one at a time
  This sequence is the system’s physical control flow (or flow of control)
Physical control flow
Time

## Slide 15: What alters the Control Flow?
CSCE-313 Spring 2017
Program-assisted mechanisms for changing control flow:
  Jumps and branches—react to changes in program state
  Call and return using stack discipline—react to program state
Insufficient for a useful system
  Difficult for the CPU to react to other changes in system state
    Data arrives from a disk or a network adapter
    Instruction divides by zero
    User hits control-C at the keyboard
System needs mechanisms for “exception control flow”
Notes: Imagine if you are placing an order at a counter and ask for an item NOT on the Menu. Or if you ask for the Manager. Or if you are checking out groceries and decide to pay in Canadian Dollars ☺. All of these will create some sort of exception requiring the attention of special procedures.

## Slide 16: Exception Control Flow
CSCE-313 Spring 2017
An exception is a transfer of control to the OS in response to some event (i.e., change in processor state)
User Process
OS
exception
exception processing
by exception handler
exception
return (optional)
event
current
next

## Slide 17: Types of Exceptions
CSCE-313 Spring 2017
Synchronous (i.e. aligned to an event or time)
Asynchronous (can happen without notice)

## Slide 18: Asynchronous Exceptions (Interrupts)
CSCE-313 Spring 2017
Caused by events external to processor
  Indicated by setting the processor’s interrupt pin(s)
  Handler returns to “next” instruction.
Examples:
  I/O interrupts
    Key pressed on the keyboard
    Arrival of packet from network
  Hard-reset interrupt
    Hitting reset button
  Soft-reset interrupt
    Hitting control-alt-delete to initiate restart on a PC

## Slide 19: Interrupt Vectors
CSCE-313 Spring 2017
  Each type of event has a unique exception number k
  Index into jump table (a.k.a., interrupt vector)
  Jump table entry k points to a function (exception handler).
  Handler k is called each time exception k occurs.
interrupt
vector
0
1
2
...
n-1
code for
exception handler 0
code for
exception handler 1
code for
exception handler 2
code for
exception handler n-1
...
Exception
numbers

## Slide 20: Synchronous Exceptions (Traps, Faults, Aborts)
CSCE-313 Spring 2017
Caused by events that occur as result of executing an instruction:
  Traps
    Intentional
    Examples: system calls, breakpoint traps, special instructions
    Returns control to “next” instruction
  Faults
    Unintentional but possibly recoverable
    Examples: Page Faults
    Either re-executes faulting (“current”) instruction or aborts

## Slide 21: Synchronous Exceptions (Traps, Faults, Aborts)
CSCE-313 Spring 2017
Caused by events that occur as result of executing an instruction:
  Aborts
    Unintentional and unrecoverable
    Examples: parity error, machine check
    Aborts current program or entire OS

## Slide 22: Trap Example
CSCE-313 Spring 2017
Open file
User Process
OS
exception
return
int
pop
Opening a File
  User calls open(filename, options)
    Function open executes system-call instruction: int $0x80
  OS must find or create file, get it ready for reading or writing
  Returns integer file descriptor

## Slide 23: Fault Example #1
CSCE-313 Spring 2017
User Process
OS
page fault
Create page and load into memory
return
event
Memory Reference
  User writes to memory location
  That portion (page) of user’s memory is currently on disk
  Page handler must load page into physical memory
  Returns to faulting instruction
  Successful on second try
int a[1000];
main ()
{
a[500] = 13;
}

## Slide 24: Fault Example #2
CSCE-313 Spring 2017
User Process
OS
page fault
Detect invalid address
event
Illegal Memory Reference
  User writes to memory location
  Address is not valid
  Page handler detects invalid address
  Sends SIGSEGV signal to user process
  User process exits with “segmentation fault”
int a[1000];
main ()
{
a[5000] = 13;
}
Signal process

## Slide 25: Summarizing Control Flow Exceptions
CSCE-313 Spring 2017
Events that require nonstandard control flow
Are Synchronous (Traps, Faults, Aborts) OR Asynchronous (I/O Interrupts, Hard or Soft Reset etc.)
Generated Externally (interrupts) or Internally (traps and faults)
OS decides how to handle

## Slide 26: Preview: User/Kernel (Privileged) Mode
CSCE-313 Spring 2017
User Mode
Kernel Mode
Full HW access
Limited HW access
exec
syscall
exit
rtn
interrupt
rfi
FP exception
FP Exception error
Notes: Processor routinely checks for interrupts and if one is logged, it goes back to save the state of the process it is executing and enters the kernel to service the interrupt. The service is done by entering a interrupt vector table which contains the address of the specific interrupt service routine. Once the routine is serviced the kernel gives control back to the user process.
In multiprocessor systems, only one processor has to service the interrupt from an external device.
What happens when you move a mouse pointer? Each move or point or click registers as an interrupt which is noticed by the processor which moves the control back to the Kernel to service the interrupt routine and that shows up as an action to its associated process (e.g. move of mouse pointer in the active window, or highlight of a word selected, etc.)
An alternative to Interrupt would be “polling” where the Kernel would go in a round-robin fashion to check the status of each device to see if they have an interrupt.

## Slide 27: Example: Web Server
CSCE-313 Spring 2017
syscall
wait
interrupt
RTU
syscall
wait
interrupt
RTU
syscall

## Slide 28: Content for this week
CSCE-313 Spring 2017
OS roles and its key challenges (Text: Chap. 1)
Control Flow in a modern computer system (Text: Chap. 2)
  Normal flow of commands and data versus anything that happens “out of the ordinary” .. how do we handle that?
Architectural Interface to the OS (Text: Chap. 2)
  features we design in HW to facilitate the OS to meet some key challenges

## Slide 29: Architectural Support for OS
CSCE-313 Spring 2017
Operating systems mediate between applications and the physical hardware of the computer
  Key goals of an OS are to enforce protection and resource sharing
    If done well, applications can be oblivious to HW details

## Slide 30: Challenge: Protection
CSCE-313 Spring 2017
Why do we execute code with restricted privileges?
  Either because the code is buggy or if it might be malicious
Some examples:
  A script running in a web browser
  A program you just downloaded off the Internet
  A program you just wrote that you haven’t tested yet

## Slide 31: Challenge: Resource Sharing
CSCE-313 Spring 2017
How do we ensure that resources are fairly (and efficiently) shared amongst (and utilized by) user programs?
Some examples:
  Many students running code on a department machine
  Amazon.com servicing concurrent users
  Playing a movie on a computer while typing a project report and printing a document

## Slide 32: Architectural Features i.e. features we design in HW to facilitate the OS to meet some key challenges
CSCE-313 Spring 2017
Privileged instructions
Protection modes (user/kernel)
Memory protection mechanisms
Interrupts and exceptions
System calls
Timer (clock)
I/O control and operation
Synchronization primitives (e.g., atomic instructions)

## Slide 33: Main Points
CSCE-313 Spring 2017
Dual-mode operation: user vs. kernel
  Kernel-mode: execute with complete privileges
  User-mode: execute with fewer privileges
Safe control transfer
  How do we switch from one mode to the other?

## Slide 34: Hardware Support: Dual-Mode Operation
CSCE-313 Spring 2017
Kernel mode
  Execution with the full privileges of the hardware
    E.g. Read/write to any memory, access any I/O device, read/write any disk sector, send/receive any packet
User mode
  Limited privileges
  Only those granted by the operating system kernel
On the x86, mode stored in EFLAGS register
Notes: Obviously, you need the part that has full rights to be really reliable!

## Slide 35: A Model of a CPU
CSCE-313 Spring 2017

## Slide 36: A CPU with Dual-Mode Operation
CSCE-313 Spring 2017

## Slide 37: Hardware Support: Dual-Mode Operation
CSCE-313 Spring 2017
Privileged instructions
  Available to kernel
  Not available to user code
Limits on memory accesses
  To prevent user code from overwriting the kernel or each other
Timer
  To regain control from a user program in a loop

## Slide 38: Privileged Instructions
CSCE-313 Spring 2017
A select few CPU instructions available only to the OS
  Allows access to protected state
  Perform global operations

## Slide 39: Privileged Instructions - Examples
CSCE-313 Spring 2017
Only the OS should be able to
  Directly access I/O devices (disks, printers..)
    Allows OS to enforce security and fairness
  Manipulate memory management state
    E.g., page tables, protection bits, TLB entries, etc.
  Adjust protected control registers
    User   Kernel modes or Raise/Lower interrupt level
  Execute the halt instruction

## Slide 40: Question
CSCE-313 Spring 2017
What should happen if a user program attempts to execute a privileged instruction?

## Slide 41: Memory Protection
CSCE-313 Spring 2017
Memory management hardware provides protection. Examples:
  Base and limit registers
  Page table pointers, Page Protection, Translation Lookaside Buffer (TLB)
Manipulating memory management hardware uses protected (privileged) instructions

## Slide 42: Memory Protection - Example
CSCE-313 Spring 2017

## Slide 43: Hardware Timer
CSCE-313 Spring 2017
Operating system timer is a critical building block
  Many resources are time-shared; e.g., CPU
  Allows OS to prevent infinite loops
Fallback mechanism by which OS regains control
  When timer expires, generates an interrupt
  Handled by kernel, which controls resumption context
    Basis for OS scheduler; more later…
  Setting (and clearing) a timer is a privileged instruction

## Slide 44: Question
CSCE-313 Spring 2017
For a “Hello world” program, the kernel must copy the string from the user program memory into the screen memory. Why must the screen’s buffer memory be protected?

## Slide 45: User  Kernel Mode Switch
CSCE-313 Spring 2017
From user-mode to kernel-mode
  Interrupts
    Triggered by timer and I/O devices
  (Synchronous) Exceptions
    Triggered by unexpected program behavior
    Or malicious behavior!
  System calls (traps) (aka protected procedure call)
    Request by program for kernel to do some operation on its behalf
    Only limited # of very carefully coded entry points

## Slide 46: Kernel  User Mode Switch
CSCE-313 Spring 2017
From kernel-mode to user-mode
  New process/new thread start
    Jump to first instruction in program/thread
  Return from interrupt, exception, system call
    Resume suspended execution
  Process/thread context switch
    Resume some other process
  User-level upcall
    Asynchronous notification to user program by the kernel

## Slide 47: Transfer from User to Kernel Mode – Handling Interrupts
CSCE-313 Spring 2017
On interrupt (x86)
  Save current stack pointer
  Save current program counter
  Save current processor status word (condition codes)
  Switch to kernel stack; put SP, PC, PSW on stack
  Switch to kernel mode
  Vector through interrupt table
  Access the interrupt handler

## Slide 48: Before
CSCE-313 Spring 2017

## Slide 49: During
CSCE-313 Spring 2017

## Slide 50: After
CSCE-313 Spring 2017

## Slide 51: At the end of handler
CSCE-313 Spring 2017
Handler restores saved registers
Atomically return to interrupted process/thread
  Restore program counter
  Restore program stack
  Restore processor status word/condition codes
  Switch to user mode

## Slide 52: Kernel System Call Handler
CSCE-313 Spring 2017
Locate arguments
  In registers or on user stack
Copy arguments
  From user memory into kernel memory
  Protect kernel from malicious code evading checks
Validate arguments
  Protect kernel from errors in user code
Copy results back
  into user memory

## Slide 53: System Calls
CSCE-313 Spring 2017

## Slide 54: Summary: User/Kernel (Privileged) Mode
CSCE-313 Spring 2017
User Mode
Kernel Mode
Full HW access
Limited HW access
exec
syscall
exit
rtn
interrupt
rfi
FP exception
FP Exception error
Notes: Processor routinely checks for interrupts and if one is logged, it goes back to save the state of the process it is executing and enters the kernel to service the interrupt. The service is done by entering a interrupt vector table which contains the address of the specific interrupt service routine. Once the routine is serviced the kernel gives control back to the user process.
In multiprocessor systems, only one processor has to service the interrupt from an external device.
What happens when you move a mouse pointer? Each move or point or click registers as an interrupt which is noticed by the processor which moves the control back to the Kernel to service the interrupt routine and that shows up as an action to its associated process (e.g. move of mouse pointer in the active window, or highlight of a word selected, etc.)
An alternative to Interrupt would be “polling” where the Kernel would go in a round-robin fashion to check the status of each device to see if they have an interrupt.

## Slide 55: Example: Web Server (Revisited)
CSCE-313 Spring 2017
syscall
wait
interrupt
RTU
syscall
wait
interrupt
RTU
syscall

## Slide 56: Summary of Learnings
CSCE-313 Spring 2017
OS roles and its key challenges (Text: Chap. 1)
Control Flow in a modern computer system (Text: Chap. 2)
  Normal flow of commands and data versus anything that happens “out of the ordinary” .. how do we handle that?
Architectural Interface to the OS (Text: Chap. 2)
  features we design in HW to facilitate the OS to meet some key challenges

## Slide 57: A Real-Life Analogy (Approximate)
CSCE-313 Spring 2017
A Typical Coffee Shop | Computer System
Store | System
Customer | Process or Program or User Application
Barista/Cashier | Operating System Kernel, Privileged Code
Coffee Machine | CPU
Customer Order | System Call
Order item not on Menu | Exception
Telephone Call | Interrupt
Fire Alarm | Signal
>1 Customers being served | Process Scheduling
Customer realizing at the counter that he needs to go to ATM to get money | Process Context Switching

## Slide 58: Next Week
CSCE-313 Spring 2017
Process and Programming Interface
Application Programs/Processes
storage
Processor
Memory
user1
user2
user3
user4
return
System calls,
Exceptions
Bock I/O
INT
Character O/P
Privileged
Operations
user1
user2
user3
user4
System calls,
Exceptions